## Slide 1: Torque at 90o
This has NOTHING to do with torque but it comes up when you google images…go figure.

## Slide 2
A body in translational equilibrium will have no acceleration in the x or y directions. However it still could be accelerating.
Consider a teeter-totter, with a 100 kg student on one end and a 50 kg student on the other.
Although the net translational forces are zero, the system has a net torque, so it is not in equilibrium.
An object in equilibrium must have both translational and rotational equilibrium.
What are the net translational forces in:
The x-direction? ____________ The y-direction? ____________
100
50

## Slide 3
The second condition of equilibrium is that in order to have no rotation, there must be no net torque.
Torque is defined as: force x distance to pivot
τ = Fd
Unit of torque: N·m

## Slide 4
Ex:
A torque of 24.0 Nm is needed to tighten a nut. If a person can apply a force of 100 N, what is the minimum length of wrench that is required?

## Slide 5
Torque is a vector quantity, which must work in either the clockwise (c) or counterclockwise (cc) directions.
If an object is in rotational equilibrium then:
Στ = 0 or τc = τcc
A few more terms we need to learn before we go on…
Centre of Gravity: The position where the average weight of the object acts.
Uniform Beam: a beam of uniform shape and density
Arbitrary Position of Rotation: we can choose any point on an object and treat it as the point of rotation.

## Slide 6
Ex: A 350 N store sign hangs from a pole of negligible mass. The pole is attached to a wall by a hinge and supported by a vertical rope. What is the tension in the rope?
Jen + Eric Store
1.3 m
2.0 m
Extension:
What are the vertical and horizontal components of the supporting force provided by the hinge?

## Slide 7
Ex:
Two students sit on opposite sides of an 800 N teeter-totter. Student 1 has a mass of 65 kg and sits at the very end of the teeter-totter. Student 2 has a mass of 90 kg. How far from the pivot should he sit in order to achieve equilibrium?
2.6 m

## Slide 8
Ex:
A 3500 kg truck is parked on a bridge a shown. If the bridge deck itself has a mass of 6500 kg find the supporting force provided by each of the two support posts.
15 m
5 m