## Slide 1: Efficiency
vs.

## Slide 2: Efficiency is a measure of how much energy is wasted by a machine.
Machines are useful because they allow us to use less force over a longer distance to do the same work.

## Slide 3: Machines always waste some energy.
The 2nd Law of Thermodynamics states that whenever work is done, some energy is converted to heat.
Therefore:
Win > Wout
Work in: Energy supplied to the machine.
Work out: Work actually done by machine.

## Slide 4: The efficiency of a machine is:
or
There are no units for efficiency, it is simply expressed as a percentage.
Efficiency = Wout x100%
Win
Efficiency = Pout x100%
Pin

## Slide 5: Example:
50.0 kg
75 N
A lever is used to lift a 50.0 kg object 10.0 cm. To do this we must apply a force of 75 N to the end of the lever which displaces 1.00 m. Find the efficiency.
50.0 kg
1.00 m
0.100 m